## Slide 1
Robotic Harvest for Elderberry – Machine Vision
Gian Lucca Teixeira (Undergraduate Researcher), Jianfeng Zhou (Assistant Professor)
University of Missouri, Columbia, MO (contact: gat7hb@umsystem.edu)
Object Detection on Elderberry
Future work
  Continue to label the elderberry dataset in order to improve the detection rate
  Implement classification CNN model to classify the state of ripeness
  Utilize depth camera to determine the optimal cut pose
  Fully integrate a robotic harvesting system, picking to packing elderberries
Elderberry Detection Results
Robotic Elderberry Harvester
  Multiple-pass harvest needs more labor
  Manual harvest efficiency can be improved
  Expensive, insufficient labor, and safety
  Need efficient solutions for advancing American elderberry
Introduction
    Selective harvest solution
    Potential to address labor issues for fruit crops
    Expensive solution and low efficiency for picking single fruits
    Have been tested in strawberries, apples, grapes …
    Potential to be used for cluster fruits, like elderberry
Summary
  Robotic harvesting system is promising for elderberry harvesting
  Implemented the use of machine vision and deep learning to detect elderberry clusters
  Developed a data collection system that acquired 2000 frames of elderberries
Summary and Future Work
Data collection system (Intel RealSense connected to Raspberry Pi 4 inside of the control box)
Raspberry Pi 4 control box running Intel’s SDK to control the cameras
RGB frame captured by the data collection system
YOLOv7 architecture
  Metrics:
    Best mAP@.5: 84% (detection confidence level of 50%)
    Best mAP@.95: 45% (detection confidence level of 95%)
    Max precision: 89%
    Max recall: 83%
Model inference with confidence levels
  Study existing berry automated harvesters and elderberry characteristics
  Develop robotic solutions for selective harvest
Objectives
Labor issues and efficient harvest
Robotic solutions
Data Collection Method
Fruit detection system
Robot Arms
Auto-guidance system
Fruit bins
A
A
B
C
D
B
C
D
Harvest system:
  Berry identification system based on machine vision
  Robotic arm with cutter and grabber
  Autonomous systems
Elderberry recognition system:
  Two stereo depth cameras to detect berry cluster’s pose
  Classify cluster ripeness with machine learning algorithms
  Identify the optimal cut position
Camera system tested in lab
  State of Art in single-stage object detector.
  Model is able to predict with real-time speed.
  Extracted 104 RGB images from the elderberry dataset and labeled all clusters manually.
  Trained YOLOv7 with 104 .jpg images with size 640x640.
  Able to detect with an intersection over union (IoU) of 83%
YOLOv7 model:
  Intel RealSense D435i depth camera
  Raspberry Pi 4
  LCD display and 26800mAH battery bank
Data collection system:
  Collection during the entire month of August
  Around 2000 frames captured
  BAG file format
    Aligned frames + Metadata
    RGB information
    Depth information
Collection method:
  Ground Truth
    Color stand for ripeness color reference
    Manually accessed ripped clusters.
    XYZ manually measured (camera as reference frame)
Important measurements graphs
  Training:
    Min box loss: 3%
    Min object loss: 1.5%
  Validation:
    Min box loss: 5.8%
    Min object loss: 2.7%